## Slide 1
ER. MOHIT MISHRA
ASSOCIATE PROFESSOR(CS DEPT)
ACEIT JAIPUR
8085 Addressing
Modes

## Slide 2: Addressing Modes
The number & Different kind of ways the programmer can
refer to data stored in the memory
The different ways that a microprocessor can access data
are referred to as Addressing modes
    Immediate Addressing mode
    Register Addressing mode
    Direct Addressing mode
    Indirect Addressing mode
    Implied Addressing mode
Addressing Modes

## Slide 3: Immediate Addressing Mode
  8 or 16 bit data can be specified as a part of Instruction
  The instruction having ‘I’ (Immediate) letter fall
  under this category
  Examples :
  MVI C,25H
  MVI M,7CH
  LXI D,245EH
  ADI 87H
Immediate Addressing Mode

## Slide 4: Register Addressing Mode
  Data transfer between Registers
  Specifies the Source ,Destination or Both Operand in an 8085 registers
  Faster Execution (it is not necessary to access memory locations )
  Examples :
  MOV A,B
  ADD E
  SPHL
  XCHG
  INR L
Register Addressing Mode

## Slide 5: Direct Addressing Mode
  Specifies 16 bit address of the operand within instruction itself
  Second & third bytes of instruction contain 16 bit
  Note : In interface IO port address is only 8 bit
  Examples :
  LDA 2000H
  LHLD 1111H
  IN 75H
Direct Addressing Mode

## Slide 6: Indirect Addressing Mode
  The memory address where the operand located is specified by the contents of a register pair
  Examples :
  LDAX B
  MOV M,D
  Immediate Indirect MVI M,55H
  Register Indirect ADC M [A A +Cy+(M)]
  DCR M [(HL)(HL)+1]
  PUSH PSW
Indirect Addressing Mode

## Slide 7: Implied Addressing Mode
  Opcode specifies the address of the operands
  Examples :
  CMA ( A A )
  STC (Cy 1)
  RAL
  DAA
Implied Addressing Mode

## Slide 8: NULL Addressing Mode
  Machine Control group
  Examples :
  EI DI
  NOP HLT
  SIM RIM
  Answer : NULL Addressing Mode
NULL Addressing Mode