## Slide 1: Wireless Technologies (WiMAX and Wireless Metropolitan-Area Networks)
Prepared By: Er. Amit Kr. Tewari
Associate Professor
CS Dept.
ACEIT, Jaipur

## Slide 2: Introduction
Metropolitan-area networks (MANs) are primarily fiber-optic networks, most often SONET rings, that connect enterprise LANs to WANs.
Another typical MAN is a local cable TV network.
Now there is wireless contender for metropolitan-area networking. Known as WiMAX, it is the wireless system defined by the IEEE 802.16 standard.

## Slide 3: Introduction
It was developed to provide a wireless alternative to consumers for broadband Internet connections.
These connections are now dominated by cable TV and DSL, but with the new WiMAX standard, wireless Internet service providers (WISPs) may soon be offering wireless broadband connections.

## Slide 4: IEEE 802.16-2004 or 802.16d
Its primary applications will fit into two basic categories: point-to-point (P2P) or point-to-multipoint (PMP).
Common examples are cell site backhaul from a base station to the switching office or Wi-Fi hot spot interconnections to the ISP.
Both of these applications typically rely on hardwired T1 or T3 connections, which are very expensive.

## Slide 5: point-to-multipoint (PMP)
The PMP mode is a broadcast mode from a central base station to multiple surrounding nodes. In this mode, WiMAX serves as a WISP for homes or businesses.

## Slide 6: WiMAX Features
WiMAX was designed to operate anywhere in the 2- to 6-GHz range wherever appropriate spectrum is available.
The spectrum may be licensed or unlicensed depending upon its location and the host country.
The most common bands are 2.3, 2.5, and 5.8 GHz in the United States and 3.5 GHz in Europe, Asia, and Canada.

## Slide 7: WiMAX Features
The maximum data rate is 75 Mbps, but that is usually divided up among a large number of users. Speed is set by bandwidth, which can be anything from 1.75 to 20 MHz.
The maximum data rate is 75 Mbps, but that is usually divided up among a large number of users. Speed is set by bandwidth, which can be anything from 1.75 to 20 MHz.

## Slide 8: WiMAX Features
The WISP will allocate bandwidth and speed to users based on their needs and charge accordingly.
Full duplex using time-division duplexing (TDD) or frequency-division duplexing (FDD) is supported by the standard.
WiMAX uses a 256-carrier OFDM system with adaptive modulation.

## Slide 9: WiMAX Features
WiMAX uses a 256-carrier OFDM system with adaptive modulation.
OFDM is a superior method that tackles the line-of-sight (LOS) problems that occur in serving a large area.
The modulation method of each OFDM channel is selected automatically depending upon the range, noise, and data rate.

## Slide 10: WiMAX Features
The standard supports BPSK, QPSK, 16-QAM, 64-QAM, and 256-QAM.
BPSK would be selected for longer range and lower speeds; 64-QAM or 256-QAM would be selected for shorter ranges to give higher speeds

## Slide 11: Mobile Version of WiMAX
The standard is IEEE 802.16e 2005
It is designed to permit nodes to be mobile while maintaining contact with a base station.
An example is a WiMAX-enabled laptop on a commuter train or in a car.

## Slide 12: Mobile Version of WiMAX Features
The maximum range is about 3 mi, but that will depend upon the environment and terrain. Speeds up to about 75 mi/h can be accommodated.
Data rates are adaptable to the environment and range but can hit a maximum of 15 Mbps under ideal conditions.
IEEE 802.16e uses 2048-channel OFDM to achieve these characteristics.

## Slide 13: Mobile Version of WiMAX Features
The access method is OFDMA (access) where the 2048 channel OFDM signal is divided among multiple users.
With 64 channels assigned to each subscriber, one OFDMA bandwidth can accommodate up to 32 users.